## Slide 1: Delay Estimator
A Forecasting Tool for New Jersey Train Delay
Jasmine Siyu Wu and Zoe Yoo

## Slide 2: Scope
Initial idea to develop delay estimates for Amtrak and NJ online ticketing
Similar geographies, but data constraints
  No scheduling times in Amtrak data
Photo sources: Amtrak, NJ Transit

## Slide 3: NJ Transit
New Jersey system differs from Amtrak
  One-way tickets or passes, with no expiration date
  Ticket prices vary based on distance but not time of reservation
Tickets can only be bought on the NJ Transit Mobile App or in-person
Trip Planner gives users scheduled trains based on date and time

## Slide 4: Trip Option Delay
Each time option shows the total predicted delay for that trip
Red = >30 minutes combined predicted delay
Orange = 20-30 minutes combined predicted delay
Yellow = 10-20 minutes combined predicted delay

## Slide 5: Detailed Trip View
Each leg of trip shows predicted possible delay
Categorized below and summed for the overall trip
Note: current data is only commuter rail, not light rail
Red = >30 minutes predicted delay
Orange = 20-30 minutes predicted delay
Yellow = 10-20 minutes predicted delay

## Slide 6: Data Structure
NJ Transit DepartureVision Real Time Train Status Service
  Aggregated on Kaggle by Pranav Badami
Sample months: January and February 2021
Spatial Data
Start Station Name and ID
End Station Name and ID
Stop Sequence Number
Line Name
Temporal Data
Scheduled Time of Departure
Actual Time of Departure
Calculated Delay (minutes)
Date
Basic Data
Train ID
Type (Amtrak or NJT)

## Slide 7: Reviewing the Data
Is delay often / severe enough to warrant a tool for it?

## Slide 8: On Time
On time: % of trains arriving at the scheduled time at each station stop on a journey
Definition source: Southern Railway, “Train service punctuality and reliability”

## Slide 9: Public Performance Measure (PPM)
Public performance measure (PPM): % of trains arriving at their destination within 5 minutes of schedule
Philadelphia-Atlantic City Line has the lowest PPM
Definition source: Southern Railway, “Train service punctuality and reliability”

## Slide 10: Regression Model
Four different models:
Time – time of day, day of the week
Space – origin and destination stations
Time, Space, Weather – (temperature/precipitation)
Time, Space, Weather, + Time Lag
Split: Train on first five weeks, test on last three

## Slide 11: Results
Greater computing power
  Use a larger sample size of data to ideally gain more accuracy year-round
Improve on the current model
  Add more variables, e.g. Number of previous stops
  Add more independent data
Improving Accuracy

## Slide 12: Future Possibilities
Increase scope
  Find scheduling data for Amtrak
  Expand data scope to SEPTA or NJ light rail, which connect to NJ Rail Transit
Other uses
  Use to figure out the possible causes delay, and how to mitigate it, before it has the chance to affect customers